## Slide 1
VisionGuard
AI Safety Monitoring System for Construction Sites
Shimaa Gomaa
Computer Vision · Object Detection · Transfer Learning
September 2026
Person 0.86
Hardhat 0.94
NO-Safety Vest 0.80
Notes: 15 sec

## Slide 2
The Problem
2
Construction sites are dangerous
Serious risks: falls, head injuries, accidents
Hardhats protect against falling objects
Safety vests keep workers visible
Manual monitoring doesn't scale
Expensive: needs dedicated safety officers
Inconsistent: human attention varies
Reactive: violations are found too late
Our solution: automate PPE compliance monitoring with computer vision.
Notes: 45 sec

## Slide 3
Project Objectives
3
What VisionGuard does
Detects workers and PPE in real time
Identifies violations: missing helmet or vest
Reports compliance statistics
Exposes results through an API and a UI
Classes | 5: Person, Hardhat, NO-Hardhat, Safety Vest, NO-Safety Vest
Input | Images, videos, live camera
Output | Bounding boxes + compliance reports
≥ 0.70
mAP50 on the test set
API + UI
working end to end
10 cases
documented error analysis
Notes: 45 sec

## Slide 4
Dataset
4
Construction Site Safety Image Dataset
Roboflow via Kaggle · CC BY 4.0
2,801 images, all 640×640 (verified)
Split | Images | Share
Train | 2,605 | 93%
Valid | 114 | 4%
Test | 82 | 3%
Classes reduced from 10 to 5
ID | Class | Purpose
0 | Hardhat | PPE present
1 | NO-Hardhat | Violation
2 | NO-Safety Vest | Violation
3 | Person | Detection
4 | Safety Vest | PPE present
Notes: 45 sec

## Slide 5
Data Challenges
5
Class | Count | %
Person | 9,532 | 26.5
NO-Safety Vest | 3,962 | 11.0
Hardhat | 3,145 | 8.8
Safety Vest | 3,033 | 8.4
NO-Hardhat | 2,317 | 6.4
4×
more Person samples than NO-Hardhat
Leakage check
Filename prefixes compared across splits: 2.47% overlap, safe.
Empty labels
Train 6 · Valid 10 · Test 8. Kept as negative samples.
Out-of-domain images
6 book covers, 1 Star Trek scene. Documented as a limitation.
Notes: 45 sec

## Slide 6
AI Approach
6
Model | YOLOv8s (Ultralytics)
Parameters | 11.1M
GFLOPs | 28.4
Pre-trained on | COCO (80 classes)
Fine-tuned on | Our 5 classes
Why YOLOv8s?
Balanced accuracy and speed
Transfer learning from COCO
Strong on small objects
Fast inference, ~10 ms on GPU
Why not a pre-trained API?
No ready-made PPE detection model exists.
The project requires custom training, and YOLOv8s is trainable and adaptable.
Notes: 45 sec

## Slide 7
Methodology
7
Raw data
›
Preprocessing
›
Training
›
Evaluation
›
Deployment
Preprocessing and training
Remap 10 classes to 5, remove out-of-scope labels, generate data.yaml
Transfer learning from COCO weights
35 epochs · batch 16 · imgsz 640
Augmentation: mosaic, flip, HSV
Deployment
FastAPI · Streamlit · WebRTC
Compliance logic: Point-in-Box
A PPE item counts for a person if its center falls inside the Person box.
Why not IoU?
Person (300×500) + Hardhat (40×30) gives IoU below 0.05 even when the match is correct.
Notes: 45 sec

## Slide 8
Experiments
8
Run | Model | Epochs | Augmentation | mAP50 | mAP50-95
Baseline | YOLOv8n | 0 | None | 0.003 | 0.001
Exp 1 | YOLOv8n | 25 | Default | 0.773 | 0.437
Exp 2 | YOLOv8n | 35 | Aggressive | 0.714 | 0.323
Exp 3 (best) | YOLOv8s | 35 | Default | 0.830 | 0.534
Exp 1: strong baseline
mAP50 0.773, which is 270× better than the zero-shot baseline.
Exp 2: too much augmentation
mixup + degrees=15 + scale=0.6 dropped mAP50 to 0.714. More is not better.
Exp 3: bigger model wins
YOLOv8s (11M params) reached 0.830 on validation and 0.811 on the test set.
Notes: 60 sec

## Slide 9
Results on the Test Set
9
0.811
mAP50
0.517
mAP50-95
0.903
Precision
0.777
Recall
mAP50 per class
Chart: 
| Hardhat | Safety Vest | Person | NO-Safety Vest | NO-Hardhat
mAP50 | 0.941 | 0.908 | 0.861 | 0.796 | 0.547
Notes: 60 sec

## Slide 10
Error Analysis
10
Error type | Count
False positives | 5
False negatives | 7
Misclassifications | 2
Root cause | Count
Crowded scenes | 3
Small objects | 3
Unusual context | 3
Challenging lighting | 2
Case 3: tunnel
A yellow hardhat on yellow machinery was missed, causing a false "Missing Helmet" alarm.
Case 6: 15 workers
9 persons missed because NMS removed valid detections in the crowd.
Case 9: bookstore
False positives, caused by non-construction images in the dataset.
Notes: 60 sec

## Slide 11
System Architecture
11
Streamlit UI · port 8501
Image · Video · Live
▼
FastAPI backend · port 8000
POST /analyze · /analyze-video
▼
ML pipeline
YOLOv8s → detections → compliance
Component | Purpose
Streamlit | User interface (4 tabs)
FastAPI | REST API backend
WebRTC | Real-time camera inference
YOLOv8s | Object detection
Compliance logic | Violation decision
Notes: 30 sec

## Slide 12
Live Demo
12
1
Image analysis
Upload an image and get a compliance report.
2
Video analysis
Upload a video and get unique persons and violations.
3
Live camera
Real-time detection from the webcam.
UI: localhost:8501
API docs: localhost:8000/docs
GitHub: github.com/shimaagomaa446-sys/VisionGuard
Notes: Live demo: 3-5 min. Keep screenshots ready as a backup.

## Slide 13
Limitations
13
Model
Crowded scenes (>10 workers): accuracy drops
Small objects (<2% of image): hardhats missed
NO-Hardhat mAP50 = 0.547 (class imbalance)
Non-construction images cause false positives
System
Real time only ~3–8 FPS on CPU
Video sampled every 5 frames
Test set of 82 images is small
Compliance logic
Point-in-Box struggles with overlapping persons
False negatives become false alarms
No temporal smoothing for video
Honest assessment
NO-Hardhat at 0.547 is not acceptable for production. Missing 41% of violations is critical in a safety application.
Notes: 45 sec

## Slide 14
Future Work
14
Model
Train YOLOv8m/l
Higher resolution (800–1024)
Augmentation aimed at crowds
Hard negative mining
Fix NO-Hardhat imbalance
System
Temporal smoothing
TensorRT, 5–10× faster
Auto-refresh live summary
Email / SMS alerts
Data
Remove out-of-domain images
More NO-Hardhat samples
More crowded scenes
Gloves, goggles, masks
Notes: 45 sec

## Slide 15
Conclusion
What we delivered
Custom-trained YOLOv8s, not a pre-trained API
mAP50 = 0.811 on the test set
Full pipeline: data → training → deployment
10 documented failure cases
Key achievements
270× over the zero-shot baseline
Point-in-Box beats IoU for small PPE
Object tracking for person counting
Critical assessment
Functional, but not production-ready. NO-Hardhat needs work, crowded scenes are hard, and CPU speed is limited.
VisionGuard shows AI can assist safety officers on site. With refinement, it could be deployed in real environments.
Notes: 30 sec

## Slide 16
Thank you
Questions?
Shimaa Gomaa
GitHub: github.com/shimaagomaa446-sys/VisionGuard
Kaggle: kaggle.com/shimaagomaa88
Model: kaggle.com/datasets/shimaagomaa88/visionguard-model-v1
Notes: 15 sec